## Slide 1: 2018 CSC Design Presentation
UMD R & Diesel Engineering Team

## Slide 2: Who We Are
Samuel Wick – President
Blake Thurnbeck – Engine Packaging
Karter Klingsporn – Fuel Management
Tucker Johnson – Electrical Lead

## Slide 3: Goals
Build Clean, Quiet, and Efficient Diesel Powered Snowmobile
Utilize stock arrangements for engine and chassis
Create a snowmobile that fulfills market needs

## Slide 4: Engine Selection
Mercedes OM 660
799 cc with an output of 40 HP at 3800 RPM
Common Rail- Direct Injection
Turbocharged
Weight to Performance improvement over mechanical injection

## Slide 5: Engine Adaptations
Engine Mounts
Drive train
Alternator and Water Pump

## Slide 6: Mercedes OM 660
Displaced volume | 799 cc
Stroke | 79 mm
Bore | 65.5 mm
Cylinder Angle | 45°
Compression ratio | 18:1
Number of Cylinders | 3 in-line
Dry Weight | 86.18 kg (190 lbs.)
Est. Running Weight | 90.71 kg (200 lbs.)
Rated Output | 33 kW @ 3800 RPM
Rated Torque | 110 N*m @ 2000 RPM
Camshaft Configuration | Overhead-single
2018 UMD R & Diesel

## Slide 7: Chassis Selection
Axis Chassis
Polaris Titan SP
Alpha Transmission
Towing Capabilities
2018 UMD R & Diesel

## Slide 8: Engine Packaging
Cooling Package
Intake Air System
Limited Hood Space
Auxiliary Oil Pump
Fuel Supply
2018 UMD R & Diesel

## Slide 9: Exhaust
Catalytic Converter
Passive Diesel Particulate Filter
Heat Isolation
  Exhaust Wrap
  Aerogel Shields
2018 UMD R & Diesel

## Slide 10: Wiring and Computer
Specialty Components Delta 400 ECU and Piezo Injector Driver Module
SX Tune
Combining Wiring Harness of Engine and Snowmobile
2018 UMD R & Diesel

## Slide 11: Unexpected Challenges
Oil Relocation
Faulty Injector
Failing Injector Driver Module
2018 UMD R & Diesel

## Slide 12: Summary
Mercedes OM660 mounted in Polaris Titan SP
Custom cooling pack to maintain engine temperatures under heavy loads
Oxidation Catalyst used to reduce CO levels by up to 90%, HC up to 80% and PM up to 20%
DPF installed to reduce soot
Maintained original geometries
2018 UMD R & Diesel

## Slide 13: Thanks!
2018 UMD R & Diesel