## Slide 1: University of Minnesota Duluth 2015 SAE Clean Snowmobile Challenge
Presented by:
Dylan Dahlheimer
Ryan Schefers
Brenden Bungert
Mark Boeckmann
UMD
University of Minnesota Duluth
Notes: Brandon

## Slide 2: Snowmobile Overview
2015 Arctic Cat ZR 7000 RR
Lightweight ProCross Chassis
Yamaha Genesis 130 FI
1049cc over 3-cylinders
EPA rated: 124 horsepower
Non-BAT compliant
UMD
University of Minnesota Duluth
Notes: Joe

## Slide 3: Marketing Appeal
Emissions reduction
Decreased sound
Outstanding performance
Integrating Flex-Fuel capabilities
More power to the ground
Reliability validation
UMD
University of Minnesota Duluth
Notes: Brandon

## Slide 4: Engine Control Methods
Standalone ECU
  Performance Electronics PE3 ECU
Wide-Band O2 Sensor
Flex Fuel Sensor
Temperature based compensations
Lambda based tuning
UMD
University of Minnesota Duluth
Notes: Kyle L

## Slide 5: Tuning Strategies
MBT ignition timing
Optimized air/fuel ratio
Reduced BSFC by 11.5%
4% increase in Volumetric Efficiency
UMD
University of Minnesota Duluth
Notes: Kyle L

## Slide 6: Dynamometer Testing
UMD
University of Minnesota Duluth
Notes: Kyle L

## Slide 7
Cooled Exhaust Gas Recirculation
Controlled from PWM motor
Sourced from Toyota Prius
Stacked style cooler
Load and RPM controlled through ECU
Integrated into exhaust pre-catalyst
Reduced NOx by 64%

## Slide 8: Emissions
Heraeus 3-way Catalyst
  HeraPur Coating
  Platinum, Palladium, and Rhodium
  105 mm Diameter, 74.5 mm Length
Integrated heat shielding
Reduced Constituents
  41.5% reduction in CO
  53.6% reduction in HC
UMD
University of Minnesota Duluth

## Slide 9: Noise Reduction
Muffler Redesign
  Stock resonator tubes
  Lined with fiberglass
  Increased backpressure
Inline baffle
SAE J192 Results: 77.9 dBA
Dynamat placement
UMD
University of Minnesota Duluth
New Design:
Stock:
Notes: Kyle S

## Slide 10: Drive Sprocket
Carbon Fiber filled Nylon 11
Ball bearing contact
2.52” Drive Pitch
Efficiency Increase of 6% through driveline
Incorporated braking lugs
Design FOS of 3
Reduction of 2.75 lbs. rotating mass from 2014
UMD
University of Minnesota Duluth
Notes: Brandon

## Slide 11: Chassis Dynamometer
10 hp electric motor
Variable Frequency Drive control
Water brake loading
Digital speedometer readout
Power input vs speed output curves
UMD
University of Minnesota Duluth
Notes: Dylan

## Slide 12: C3 Belt Drive with Quiet Drive Track
Belt drive to replace chain case
Reduces 11 lbs. of weight and 8 lbs. of rotating mass
128” Camoplast Hacksaw Quiet Track
1.080” Woody’s studs
Reduced track weight by 5 lbs.
UMD
University of Minnesota Duluth
Notes: Brandon

## Slide 13: Overall Efficiency Improvement
6.1% Overall Improvement

## Slide 14
2015 Arctic Cat ZR 7000 RR
Standalone PE3 ECU with complete engine tune
3-way catalyst with integrated cooled EGR system
Carbon fiber roller drive sprocket
13.5% reduction in sound
6.1% driveline efficiency increase
250 Miles of on-snow validation
Fun, marketable sled with real world applications
Project Overview

## Slide 15: Thank You
UMD
University of Minnesota Duluth