## Slide 1: TEAM QUIETS-CI #103 2019 SAE CSC DESIGN PRESENTATION
By: Quentin Gravel and
Mathieu Verner

## Slide 2: Presentation content
Overall packaging
Chassis modifications
Powerplant
Drivetrain modifications
Additional features
Driver features
Possible future upgrades
Notes: Do

## Slide 3: Overall packaging
Objective : Marketable utility snowmobile
2017 Ski-Doo Tundra Sport
Kohler KDW1003
Notes: Do

## Slide 4: Chassis modifications (2017)
New S-module design
Simulated at 765 lbs (engine: 176 lbs)
Notes: Gui

## Slide 5: Powerplant
Stock engine specifications :
  Inline 3 cylinders
  1028 cc
  Mechanical fuel injection
  23.4 HP
  36.8 ft-lbs
Last year engine specifications:
  36 HP
  47 ft-lbs
  E-Score: 206
  Soot: 67
Notes: Do

## Slide 6: Powerplant
Exhaust design
  Turbo BorgWarner KP35
  Diesel Oxide Catalyst / Passive Diesel
  Particulate Filter
  900 ACE Ski-Doo Muffler
Notes: Do

## Slide 7: Powerplant

## Slide 8: Powerplant
Flywheel alternator
Air intake muffler
Notes: Do

## Slide 9: Steering column
Steering column redesign
Notes: Gui

## Slide 10: Engine mounts

## Slide 11: Drivetrain modifications
Clutches :
  Custom design
  for our application
  Operating range :
  900 to 3800 RPM
  Driving ratio :
  4:1 to 0.75:1
  Heavier weights (416g)
  and stiffer spring
Notes: Gui

## Slide 12: Drivetrain modifications
Silent Drive sprocket Chaincase ratio
Bottom chaincase gear:
  Stock : 51 tooth
    Top Speed = 45 mph
    RPM @ 35 mph = 3000
  New : 43 tooth
    Top Speed = 55 mph
    RPM @ 35 mph = 2400
Notes: Gui

## Slide 13: Additional features
Heat management
Stiffer front suspension springs
Lithium-Ion Battery
Notes: Gui

## Slide 14: Driver features
Rollerskis by Qualipièces
Reverse
Ice scratchers
2 places seat
Stability and Turning Enhancement Kit
Clip-on 3D printed cup holder for Coca-Cola and Redbull
Notes: Gui

## Slide 15: Possible future upgrades
Drive by wire throttle
110V power outlet
Oil pump with quick connects
for accessories
  Chainsaw and log splitter
  Grooming trails
  Logging trailer
  Dump trailer
  Winch

## Slide 16: Questions?