## Slide 1: TEAM QUIETS 2018 SAE CSC DESIGN PRESENTATION
By:
Pierre-Olivier Langlois
Guillaume Verner

## Slide 2: Presentation content
2018 HPDI 600 ACE
2018 600 ACE turbo
Noise and efficiency
Additional features

## Slide 3: HPDI
High pressure mechanical fuel pump
  Automotive fuel pump
  Pressure range : 500 – 2500 PSI
Custom designed cam

## Slide 4: HPDI
DI optimized piston shape
  Forged aluminum
  Increased compression ratio (12.6:1)
  Optimized shape
  Maximize fuel atomization
  Prevent cylinder wall wetting
2017
2018

## Slide 5: HPDI
New cylinder head design
Modified head to install DI injectors

## Slide 6: HPDI

## Slide 7: 600 ACE Turbo
87 octane
85 hp
60 ft.-lbs
BSFC : 375 g/kW-hr
E85
110 hp
80 ft.-lbs
BSFC : 450 g/kW-hr
Specifications

## Slide 8: 600 ACE Turbo
New catalytic converter
  Larger diameter
  Better flow
  Lower emissions

## Slide 9: Noise and efficiency

## Slide 10
Big wheels and track
  Modified track structure
  8” plastic/rubber big wheels
  15% amperage draw reduction
Chart: Return wheels comparison
| 1200 | 1800 | 2400
OEM wheels | 1.5 | 3.15 | 6.45
Alu. Big wheels | 1.3 | 2.85 | 6
Rubber big wheels | 1.3 | 2.8 | 5.95
Noise and efficiency

## Slide 11: Noise and efficiency
New drive sprocket design
  9 tooth
  Constant contact
  Drive rollers
  4% amperage draw reduction

## Slide 12: Additional features
Roller ski
  Auto retractable ski wheel system
Reverse
  Because every snowmobile should have a reverse
Ice scratcher
  Lubricate the track clips to reduce friction
  Reduce coolant temperature on icy conditions
Adjustable ski runner depth
  Adapt to all snow conditions

## Slide 13: Questions?

## Slide 14: Noise Reduction
Big wheels and track