## Slide 1: SAE CLEAN SNOWMOBILE CHALLENGE (CSC) 2016 Team IUPUI

## Slide 2: INTRODUCTION

## Slide 3: Our University,
Located in capital of Indiana, Indianapolis
2 top universities, 1 dynamic campus
Accredited by both Indiana University and Purdue University
First university in the United States to offer a bachelor's degree in Motorsports Engineering
One of the pioneer universities to offer a bachelor's degree in Energy Engineering

## Slide 4: SNOWMOBILE DESIGN

## Slide 5: Why Electric Snowmobile?
Lighter
Quieter
More affordable
Will not contaminate core sampling
Does not pollute the environment

## Slide 6: Chassis – Polaris 550 Indy
Lightweight
Entire snowmobile only weighs 450 lb

## Slide 7: Frame
Aluminum construction
Track
15 inches in width
121 inches in length

## Slide 8: AS AN OPERATOR

## Slide 9
Converted to Electric Snowmobile
Practical choice for clean environments
15 miles range in ideal conditions.
Battery recharges in 2 hours with 220 V or 4 hours with 110 V

## Slide 10: AS A DEALER

## Slide 11
Minimal service required
Durable design based on Continental SilentSync belt
Low MSRP: $12,999
Easy to drive
No special switches

## Slide 12: Cost Breakdown for Major Components
 | 1 Unit | 500 Units
Glider frame | $4,000 | $4,000*
Electric motor | $2000 | $550
Motor controller | $500 | $500
Battery | $3,000 | $3,000
Others | $3499 | $3,499
Total | $12,999 | $11,549
* No reduction unless partnership develops between current snowmobile manufactures.

## Slide 13: AS THE ENVIRONMENT

## Slide 14
Lightweight allows for a more efficient design
The electricity power used to recharge the batteries is more efficient than gasoline, even when using dirty coal.
Using the lightest Syncho Belt available, we made the machine quiet.
The Continental belt and pulleys produces 65 decibels

## Slide 15: TEST RESULTS

## Slide 16: Theoretical range calculation
Battery size
  3.2volts x 19.5amp hour x 72 cells = 4492.8 watt hour
  4492.8 whr/ 250 whr/mi = 17.97 miles {Best conditions}
  4492.8 whr/ 425 whr/mi = 10.57 miles {Worst conditions}

## Slide 17: Future Work
Reduce weight and increase efficiency
  More carbon fiber
  Reduce size
Increasing range and performance
  To use a higher performance lithium ion battery
Produce Reliable Phase 2 model for CSC 2017
  Pass Tech inspection
  Use of more modular components

## Slide 18: QUESTIONS?

## Slide 19: Thank you.

## Slide 21: Battery Management System with Fuse Boards
BMS Master
BMS Slave
Fuse Boards

## Slide 22: BMS Schematics (Linear LTC 6804)

## Slide 23: Range Calculations