## Slide 1: University of Wisconsin - Platteville 2014 Clean Snowmobile Team
Presenters:
Niko Bognar
Brandon Krautkramer

## Slide 2: Design Objectives
Create Efficient Snowmobile Fueled by 16%-32% Isobutanol
Emissions Reductions
  Noise
  Exhaust
Maintain Stock Riding Qualities
  Performance
  Comfort

## Slide 3: Consumer Appeal
Comfort
  Ergonomics
Reliability
High Performance
  TrailTrac
Low Maintenance
Low Operating Cost
  Fuel Mileage

## Slide 4: Dealer Appeal
Sales
  Marketable to consumers
    Aesthetics
    Performance
    Comfort
Service
  Readily available parts
  Ease of Maintenance

## Slide 5: Snowmobile Choice
Chassis: 2014 Arctic Cat ZR 7000 LXR
Model: ProCross
Engine Type | 4-Stroke
Engine Details | Liquid Cooled Genesis 130FI
Cylinders | 3
Displacement | 1049 cc
Bore x Stroke (mm) | 82mm X 66.2mm
Exhaust | Single
Fueling | Electronic Fuel Injection

## Slide 6: Design Strategy
Efficiency
  Engine Management
  Driveline Improvements
Clean
  Engine Selection
  Custom Exhaust
Quiet
  Sound Deadening Material
Flex Fuel
  Isobutanol mix 16%-32%
User Friendly
  Ergonomic Rider Position
  Trail Performance Related
  Simple Display and Controls
  Easy Starting
  Adjustable Suspension

## Slide 7: Engine Management
Performance Electronics Stand Alone ECU
  User Friendly
  Wi-fi Tuning Capabilities

## Slide 8: Engine Tuning and Calibration
DYNOmite Water-Brake Dynamometer
AFX Wide Band AFR Monitor
Exhaust Gas Temperatures
EMS Emissions Analyzer

## Slide 9: Environmental Benefits
Reducing Emissions
Tikka Race
Pre-Burn Catalytic System
  Pre-Cats
  Main Cat
Advantages
  Maintains Stock Back-Pressure
  Replaces Previous Muffler
  No Maintenance

## Slide 10: Driveline Improvements
Belt Drive System
  C3 Powersports
Replaced Drivers
  9 Tooth to 10 Tooth
Replaced Stock Rear Idler Wheel with 10 Inch Diameter Billet Wheels
Dupont Teflon Slides
Track
  Camoplast Ice Attak XT

## Slide 11: Driveline Improvement Results
Varying Driveline Configurations
Drill Test
  Hp lost = (115 Volts)*(Amps)* (0.001341 Hp/W)
  22% More Efficient
Pull Test
Throttle Position Test
  13.1% Reduction of Throttle Position at Same Speed and Conditions
Chart: Force Required (lbf)
Modification | % Reduction of TPS
Belt Drive System | 9.26
Big Wheel Kit | 2.12
Dupont Teflon Slides | 1.71
All Modifications Combined | 13.09
Chart: Pull Test for Driveline Resistance
| Stock | Stock w/ DuPont Slides | Stock w/ Belt Drive
 | 82.2 | 71 | 53.3

## Slide 12: Sound Deadening
Custom Muffler
Engine Compartment
  Polymer Technologies Acoustical Barrier with Absorber
Reduced 7 dB
Chart: Sound Deadening Properties
Average Stock dB | 86
Average dB w/ sound deadening foam and custom muffler | 79

## Slide 13: Suspension
Easily Adjustable Front and Rear Suspension
  Capable of being tuned for various riding styles
Floating Front Rear Suspension
  Improved Control in Small and Large Bumps
  Better Traction

## Slide 14: Summary
Consumer Benefits
  Comfortable / Ergonomic
    Easy and fun to ride
  Reliable
  Competitive Cost
    $15,411.72 USD MSRP
Dealer Benefits
  Easy to Sell
  Easy to Service
Environmental Benefits
  Low Emissions
  Quiet

## Slide 15: Thank You
Questions?